## Slide 1
Reaching
Net Zero
In Affordable
Housing
ENEGRY TRUST OF OREGON NET ZERO FELLOWSHIP 2021
By
Mark McKechnie, AIA
Oregon Architecture, Inc.

## Slide 2: Agenda
Introduction
Project Study in Brief
Research Tools
Research Goals
Research Team
Research Strategies
Research Results
Research Conclusions & Lessons Learned

## Slide 3: Introduction
Concept of Net-Zero
Definition of The Term Net-Zero
About The Fellowship
Net zero in energy growth is an effort to make energy production a zero-sum enterprise. The energy requirements of new users is off-set by the reduction in energy use from existing users and new supplemental sources.
Net Zero is exactly that – whatever additional energy is required by new construction is off-set by reductions from current users or provided by supplemental sources (i.e., on-site solar panels) so that additional output by power generating sources is not required.
The Energy Trust of Oregon annually awards a Fellowship to an entity involved in some way with the production or use of energy to study how or what can be done to reduce the rate of expansion on the power generation systems, hopefully reaching zero at some point in time.

## Slide 4
DAVID SOMMER
NIRANJAN PATIL
MARK MCKECHNIE, AIA, NCARB
Senior Project Manager at OAI
Architect, Principal at OAI
Design Project Manager,
Assoc .AIA, LEED Green Assoc. at OAI
Universal Technical Institute, Phoenix, AZ
Former Director of Facility & Grounds for Ashland Public Schools, OR.
University of Oregon, Bachelor of Architecture, 1972
University of Minnesota, Master of Architecture, 1978
Founding Principal Oregon Architecture, Inc. 2008
Bachelor of Architecture Chhatrapati Shivaji University, Kolhapur-IN.
Master of Science in Sustainable Design and
Master of Science in Construction Management Thomas Jefferson University, Philadelphia- PA.
Research Team

## Slide 5: Project Studies In Brief
Project: Victory Commons and Trail’s View multifamily housing projects for the Klamath Housing Authority.
Project Location: Klamath Falls, Oregon
Project Size: Duplexes, 1 Bedroom Units, 630 SF ea. Duplexes, 2 Bedroom Units, 810 SF ea.

## Slide 6: Research Tools
BEM is computer-based simulation practice software used to perform detailed analysis of energy usage within a building and its systems
Energy modeling evaluates the efficiency & performance of the building
Software/ tools : Sketchup & Sefaira by Trimble Revit, AutoCAD & Insight 360 by Autodesk

## Slide 7: Research Goals
Research to provide the Oregon Housing and Community Services Office with options to modify their standard rent/utility calculations to allow for more energy efficient construction.
Inform local Housing Authorities on a funding source to pay for additional energy efficient construction.
Factor in strategies that recognize while utility costs increase with inflation, construction costs are fixed at the time of project construction.
Provide information to builders in conventional markets that energy saving strategies can be financed in the conventional mortgage marketplace by utility savings.
Over time utility savings can provide more available funds for mortgage servicing.

## Slide 8: Research Strategies
Properties Timespan | *Victory Commons 1 BR Unit | *Victory Commons 2 BR Unit | *Trail’s View 1 BR Unit
Avg. Per Month | $52.65 | $90.05 | $78.91
Avg. Per year | $631.77 | $1080.61 | $946.90
**10 years projection | $6,917.71 | $11,503.90 | $10,368.30
**20 years projection | $15,350.35 | $25,527.00 | $23,007.18
**30 years projection | $26,774.00 | $44,524.30 | $40,129.00
**Note: Escalation rate for future electricity costs is at a 2% increase per year, based on historical data.
*Baseline units were originally constructed with some efficient energy strategies that went above the minimum Building Code energy requirements at the time of permitting.
Energy Usage Data
Chart: YEARS
| 2020 | 2030 | 2040 | 2050
T.V. | 946.9 | 1154.27 | 1407.04 | 1715.18
V.C. 2BED | 1080.61 | 1317.26 | 1605.73 | 1957.38
V.C. 1BED | 631.77 | 770.12 | 938.78 | 1144.36

## Slide 9: Raised-Heel / Energy Heel Truss
Attic ventilation
Roofing material
Fiber glass insulation
Heel truss
12”
OSB
Sheathing
Efficient use of attic insulation, especially at the narrow part of the truss
Adequate attic ventilation, thus no mold issues, better control of air infiltration
More comfortable interior
Economical method of producing a more resilient building envelope
No special training required for installation

## Slide 10: Mechanically Vented Crawl Space
Required less energy to keep the living space at comfortable temperature, hence improves indoor air quality
Helps to remove any moisture saturated with space and walls
Reduces mold & wood decay on floor joists

## Slide 11: Project Strategies
Building
Orientation
More energy efficient design, good for daylighting, summer-winter winds, sun & solar tempering.
Passive
Design
Design strategies to reduce / eliminate the load on mechanical systems.
Daylighting
Understanding the lighting needed & heat gain for interior spaces, minimize the use of artificial lighting during day time.
SIP’s Panel
Exceptional Thermal Performance, Healthier air quality, faster construction with less labor, design flexibility.
Trombe
Wall
Heat exchange concept. Works in mild climates as well as extreme cold, can be used for cooling or heating the building, aesthetically attractive

## Slide 12: Project Strategies
Weather
Seal
Airtight building envelope, cost effective, reduce the load on HVAC.
Efficient Door &
Windows
Highly insulated, low U-value, low-E,
appropriate sizes, optimized window to floor Area (WFA), high SHGC
Solar Panel
Clean & Green energy source, low maintenance, diverse application,
generates electricity to support building needs or demands
Energy Efficient
Appliances
Strategic lighting, LED lighting, Energy star rated appliances to reduce electricity consumption.
Net
Zero

## Slide 13: Strategy 1: Building Orientation
PLAN
Not To Scale
SOUTH ELEVATION
Not To Scale
Before
After

## Slide 14: Strategy 2: Daylighting Analysis
Reduce the need for artificial lighting
Reduce electricity costs
Can reduce HVAC costs as well
Enhanced indoor air quality
Enhanced thermal comfort
Improved mental & physical health
Daylight
Radiant Temperature

## Slide 15
Exceptional thermal performance
Healthier air quality
Faster construction with less labor
Design flexibility
SIPS FRAMING | 
Snap Lines | 1 Day
Plates | 1 Day
Frame | 3 Days
Plumb & Line | 1 Day
Set Beams | 1 Day
Roof Panels | 1 Day
Total | 8 Days
STICK FRAMING | 
Snap Lines | 1 Day
Plates | 1 Day
Frame | 4 Days
Plumb & Line | 2 Day
Set Beams | 2 Day
Roof Panels | 2 Day
Total | 12 Days
Note: Based on actual production builder’s 2,500 SF single homes by Primer Building Systems
SIPs Framing VS Stick Framing
@Petra Building Soulution
Strategy 3: SIP’s Panels

## Slide 16: Strategy 4: Trombe Wall
Most flexible solar option
Can work in mild climates as well as extreme cold
Provides comfortable heat
Passive design – no moving parts
Reduces glare on furniture compared to direct gain design
Significantly reduces heating bills
Simple construction
Aesthetically pleasing
Image credit: Paul Raff Studio
Image credit: Egon Vettorazzi, & Pinterest
SUMMER
WINTER

## Slide 17: Strategy 5: Weather Seal
STEP 1
Exceptional airtightness in Building envelope
Healthier air quality
Seals all crack and gaps
Eliminates leaks that degrade HVAC performance
Increased design flexibility
Faster, more reliable and potentially cheaper than air-seal by hand
Requires positive ventilation
Prep & Setup: AeroBarrier system & nozzles are setup throughout the house. Designed openings that will not be sealed are protected. (e.g. Windows)
Pressurize & Apply: The area is pressured with a modified blower door & fan and rest process is controlled by computer.
Seal & Monitor: A final blower door test is run & a report is created, documenting pre & post leakages.
Cleaning: After the seal is completed, all equipment & prep work is removed. Work can resume in 30 min.
© 2021 Aeroseal,LLC.
STEP 2
STEP 3
STEP 4

## Slide 18: Strategy 6: Efficient Door & Windows
Better insulation
Eco- friendly
Lower HVAC costs
Less damage to interior
Sound proof
Reduced maintenance
© 2021 WCMA NET Window & Door
Low-E Glass reduces heat gain From the sun in the summer, Keeping you home cooler.
In the winter, Low-E glass lets the warm solar rays in while blocking the heat in your home from getting it out.
Solar Heat
UV light
Visible light
Visible light
Warmth
SUMMER
WINTER

## Slide 19: Strategy 7: Efficient Appliances
Residential Building Energy Consumption by End Users
Source: Environmental & Energy Study Institute
Chart: 
| Space Heating | Water Heating | Space Cooling | Lighting | Refrigeration | Electronics | Wet Cleaning | Cooking | Computer | Other
Sales | 0.28 | 0.13 | 0.15 | 0.1 | 0.06 | 0.08 | 0.05 | 0.04 | 0.02 | 0.09
Source: Environmental & Energy Study Institute
Reduces energy consumption
Reduced carbon footprint & greenhouse gas emissions
Significantly reduce utility bills
Earn a great return on your investment as they last longer
Enhanced quality of life

## Slide 20: Building Analysis
Walls : R-21
Windows: U-0.35
Roof: R-38
Proposed
Baseline
Walls : R-41 SIPs
Windows: U-0.18
Roof: R-41

## Slide 21: Research Result
Baseline Construction
Net Zero Construction- Without Solar
Chart: 
| Remein | reduced
Sales | 67 | 33
67%
Reduction in energy consumption without the addition of solar panels
EUI: 38 kBTU/SF/Yr
EUI: 18 kBTU/SF/Yr

## Slide 22: Solar Energy
Zero Energy Building envelopes are extremely energy efficient, but the residual electrical demand must be provided by renewable energy sources such as solar and wind to make the building truly Net-Zero.
Source: Vivint Solar, Unsplash.com
Note: Number of solar panels is dependent on the size and the capacity of each panel
Our Considerations for site demand of 2,196 kWh per year:
Size: 5’ X 3’= 15 SF each Capacity: 280 Watts
Renewable Energy generation on site: 2,269 kWh per year number of panels: 6 panels
Chart: 
| Remein | reduced
Sales | 67 | 33
100%
100% reduction of usage of non renewable energy by adding solar panels

## Slide 23: Cost Estimation Tool
Properties Timespan | Victory Commons 1 BR Unit | Victory Commons 2 BR Unit | Trail’s View 1 BR Unit
Avg. Per Month | $52.65 | $90.05 | $78.91
Avg. Per year | $631.77 | $1080.61 | $946.90
10 Years projection | $6,917.71 | $11,503.90 | $10,368.30
20 years projection | $15,350.35 | $25,527.00 | $23,007.18
30 years projection | $26,774.00 | $44,524.30 | $40,129.00
Total cost of Net Zero construction payback in less than 30 years

## Slide 24: Cost Estimation Tool Sample

## Slide 25: Conclusions & Lessons Learned
We discovered quickly from this exercise that creating a zero energy or near-zero energy building shell is possible with the technology currently available in the marketplace and within a generally reasonable cost.
However, achieving total zero energy is a bit trickier: we will still need a way to electrically power artificial lighting, refrigeration, cooking, and electrically powered equipment. These tools of modern living are getting more efficient all the time, but no matter how efficient they become, they will still need electric power. At the moment, the only option to provide that energy is through the use of solar panels.
Our study shows it is possible to trade the purchase of energy over time to the purchase materials to make a dwelling more energy efficient initially. Our interactive cost tool provides a way that allows a person to evaluate the construction cost of an energy upgrade against the potential amount of energy saved in dollars.

## Slide 26: That concludes the Presentation. Thank you. Are there any questions?